## Slide 1: Localisation using inertial sensors and wireless networks
Peter Anderson
CSIRO summer intern
February 2012
Supervisor:
Dr Mark Johnson

## Slide 2: Background
CSIRO has developed WASP (Wireless Ad-hoc System for Positioning)
  High accuracy time of arrival (TOA) based wireless ranging
  Provides position updates of mobile nodes using surveyed stationary nodes
  Works outdoors, indoors and underground
  Applications include athlete tracking, mining & emergency services

## Slide 3: Problem
Analog Devices ADIS16405 IMU includes:
  3-axis accelerometer (measures acceleration)
  3-axis gyroscope (measures rate of turn)
  3-axis magnetometer (electronic compass)
Complementary nature of WASP and IMU:
  WASP positioning is stable in the long term but does not capture orientation or short term dynamics
  IMU’s capture short term dynamics but suffer from medium and long-term drift
Devise an algorithm to integrate data from an Inertial Measurement Unit (IMU) with position observations from WASP.

## Slide 4: Importance of WASP / IMU integration
 | WASP | WASP + inertial measurement unit
Characteristics: |  | 
Update rate | ~ 10 Hz | 820 Hz
Accuracy | ~ 0.2 m | Potential improvement
Signal loss | Uncertainty grows rapidly | 5 - 10 seconds of stable positioning
Outputs: |  | 
Position | Yes | Yes
Velocity | No | Yes
Acceleration | No | Yes
Orientation | No | Yes

## Slide 5: The challenge

## Slide 6: The challenge

## Slide 7: The challenge

## Slide 8: The challenge

## Slide 9: The challenge

## Slide 10: Approach
WASP
Kalman Filter
+
velocity error
position error
orientation error
gravity north
position
+
-
gyro bias
accelerometer bias
IMU
Navigation Equations
+
acceleration
velocity
position
orientation
+
-
Output
x
+
-
+
gravity error
north error
position error
Use a dual indirect Kalman filter
Kalman Filter: An optimal algorithm for tracking the state of a system from noisy observations
“Indirect” because it tracks errors in position, velocity and acceleration, not the actual quantities
“Dual” because it estimates both the state (navigation errors) and parameters (sensor biases) of the system
10Hz
820Hz

## Slide 11: Preliminary results
0
20
40
60
80
100
120
140
-40
-20
0
20
40
time in secs
Acc ms-2
x
y
z
0
20
40
60
80
100
120
140
-4
-2
0
2
4
time in secs
Vel ms-1
x
y
z
0
20
40
60
80
100
120
140
-40
-30
-20
-10
0
10
time in secs
Position m
x
y
z
0
20
40
60
80
100
120
140
-200
-100
0
100
200
time in secs
Roll Pitch Yaw deg
R
P
Y
2 minute outdoor person tracking:
  IMU track overlaps with WASP
  Now with velocity, acceleration & orientation outputs as well

## Slide 12: Preliminary results
Zooming in on a section of track:
  The much greater update rate of the IMU can be seen
  Plotting the orientation shows that it is generally performing ok

## Slide 13: Progress Summary
 | WASP | WASP + inertial measurement unit
Characteristics: |  | 
Update rate | ~ 10 Hz | 820 Hz
Accuracy | ~ 0.2 m | Potential improvement
Signal loss | Uncertainty grows rapidly | 5 - 10 seconds of stable positioning
Outputs: |  | 
Position | Yes | Yes
Velocity | No | Yes
Acceleration | No | Yes
Orientation | No | Yes

## Slide 14: Thank you
Contact Us
Phone: 1300 363 400 or +61 3 9545 2176
Email: enquiries@csiro.au Web: www.csiro.au
ICT / Wireless & Networking
Peter Anderson
Summer Intern
Phone: 02 9372 4429
Email: p.anderson@csiro.au
Acknowledgments
I would like to acknowledge the support and encouragement of my supervisors Mark Johnson and Thuraiappah Sathyan.

## Slide 15: Kalman filter process model

## Slide 16: Kalman filter measurement model